Name 	 Class 	 Date

Reteaching

More Multiplication Properties of Exponents

When a power is raised to another power, like (xy)z, multiply the exponents.

Problem

What is the simplified form of (d3)4?

(d 3 )4 ( d 3·4	The expression is a power, d 3, raised to another power, 4. Multiply the exponents.

( d12	Simplify.

Simplifying powers may require you to use multiple properties of exponents. You
should follow the order of operations when simplifying exponential expressions.

Problem

What is the simplified form of (n(3)6n4?

Using the order of operations, first simplify the power (n(3)6.

(n(3)6n4 ( (n(3 · 6)n4 ( n(18n4

Next, multiply. The two powers have the same base, so simplify by adding the exponents.

n(18n4 ( n(18 + 4 ( n(14

Finally, write the expression using positive exponents. Rewrite the expression using the
reciprocal of the base and the opposite of the exponent.

You should follow the same rules when simplifying numbers written in scientific
notation raised to a power.

Problem

What is the simplified form of (4.2 × 10( 7) 2 written in scientific notation?

(4.2 × 10(7 )2 ( (4.2)2(10(7)2	This is a product raised to the exponent 2, so each factor of the
product must be raised to the exponent 2.

( 17.64 × 10(14	Multiply 4.2 by itself. Multiply the exponents on the expression
with base 10.

( 1.764 × 10(13	Move the decimal point one place left and adjust the exponent on
10 to write in scientific notation.

Prentice Hall Algebra 1 • Teaching Resources

29

Name 	 Class 	 Date

Reteaching	(continued)

More Multiplication Properties of Exponents

Exercises

Simplify each expression.

| 1. (y2)3 | 2. (v9)6 | 3. (h4)5 | 4. (n4)11 |
| --- | --- | --- | --- |
| 5. (p–1)5 | 6. (z3)–6 | 7. (x–4)–5x | 8. (f 5)–1f 8 |
| 9. | 10. (6c)–3 | 11. (7k)0 | 12. |
| 13. (2y–5)3(x11y–10)2 | 14. u–9(u–1v)4u–5 | 15. (x13y6)–2(y–5x10)6 | 16. 4m0n0(6m5)2 |

Simplify. Write each answer in scientific notation.

| 17. (2 × 10–8)3 | 18. (3 × 105)3 | 19. (9 × 10–15)3 | 20. (6 × 105)2 |
| --- | --- | --- | --- |
| 21. (6.7 × 1011)2 | 22. (9.5 × 107)3 | 23. (4.7 × 10–11)–2 | 24. (5.14 × 106)2 |

25. The radius of a cylinder is 6.8 × 105 m. The height of the cylinder is
2.2 × 103 m. What is the volume of the cylinder? (Hint: V = 3.14r2h)

Complete each equation.

| 26. | 27. | 28. |
| --- | --- | --- |
| 29. | 30. | 31. |

Prentice Hall Algebra 1 • Teaching Resources

30

# Text boxes

7-3

7-3